## Slide 1
The
Archi
tects
Notes: Ramuld

## Slide 2: Agenda
Pitch
QAW Highlights
Synthesis
Prototyping
Q&A
Notes: Ramuld

## Slide 3
Pitch
Notes: Jacob

## Slide 4: Pitch
Core idea
Stock-like features
Trigger-orders
Be your own broker
Notes: Jacob

## Slide 5
Quickly register
Centralized “banking”
Overview
Notes: Jacob
Image wanting right now to be fully ready to place 200 kr. On any betting site.
It would require 9600 kr in down-payment. And imagine the cognitive overload, of quickly navigating 48 different bookmakers UI.

## Slide 6: Pitch summary
Always get shown the best bets
Only cash on a single site
Consistent bookmaker behaviour
Act on the market,
or become the market
Notes: Jacob

## Slide 7: QAW Highlights overview
Performance
Modifiability
Safety
Quality:
Scenario:
World cup
Many external bookmakers
update their odds
Many BestBets logins
Many bets to forward
Bookmaker
Remove
Add
Changing API
Bets
Odds change before confirmation
Different thresholds
Impossible: removed from bookmaker
Votes:
14
11
10
Notes: Thor

## Slide 8: Performance scenarios & styles & tactics
2: User login surge
3: Surge of bets
1: Real-Time Betting Odds Update
Pattern considered:
Event broker
Message queuing with the Actor model
Tactics considered:
Control resource demand: Prioritize whales*
In general, Introduce concurrency: Make the work embarrassingly parallelizable
"86% of online gambling profits comes from 5% of the players.“ - Les Bernal ["Raising the stakes" (2024), CBC NEWS]
Notes: Thor

## Slide 9: Modifiability Scenarios & styles & tactics
BettingId  MatchId
3: Adapt to changing bookmaker API’s
1/2: Addition and removal of bookmakers*
Pattern considered:
Microkernel
Tactics considered:
Split module & encapsulate external calls: Increases cohesion, reduces coupling.
Let each actor handle
only one bookmaker
*12 new bookmakers since 2019 [Spillemyndighederne: https://www.spillemyndigheden.dk/tilladelsesindehavere?field_license_type_target_id=All
Notes: Jacob

## Slide 10: Safety Scenarios & styles & tactics
1. Without threshold / Non-trigger order
2. With threshold / trigger order
Transactions:
Consider initial bet placement as start of transaction,
And final confirmation/rejection as end of transaction.
Pattern considered:
Tactics considered:
Actor model with message passing.
A single actor handles a complete transaction before being killed
Notes: Ramuld

## Slide 11: Trigger order & Bet placement Zooming in on the prototype
Notes: Jacob

## Slide 12: Microkernel zoomed in view
Notes: Thor

## Slide 13: Plugin actor model zoomed in view
Notes: Thor

## Slide 14: Prototyping
VS
Load balancer
Actor model
Concerns
Can the system handle
world-cup-sized events
Can a bet transaction complete fast
enough to get successfully placed
Hypothesis
Performance
  The load balancer will perform
  Better than the actor model
Safety
  The actor model will complete
  a single transaction with fewer
  retries than the load balancer.
Actions to take during AP:
Measure response time statistics
Measure average retries
Notes: Ramuld

## Slide 15: Test setup
Multiple servers / actors
Multiple clients
Microkernel Load balancer / Actor forwarder
* All are Lenovo Thinkpads T490 * All are on different networks Courtesy of Grumlebet
Notes: Jacob

## Slide 16: Threats to validity
Prototype doesn’t correctly simulate retries
Every “bookmaker” had same logic.
In real life bookmaker behaviour will vary greatly.
Local vs real network
Notes: Jacob

## Slide 17: Results
Actor model |  | Load balancer
Lower throughput | Performance | Higher throughput
Guaranteed single transaction prioritization | Safety | Complex prioritization
Notes: Ramuld

## Slide 18: Conclusion
Perhaps a combo?
Pros:
Load balancing to prevent bottlenecks
Actors give natural separation and simple prioritization
Cons:
Adds another step to the process which increases latency.
Slight increase to modifiability complexity
Notes: Thor

## Slide 19: Relevant pieces from the log
We want to zoom in on the event broker as well and make a prototype
We want to look more in-depth into the combo-solution
Notes: Ramuld

## Slide 20: Thank you
Questions?